## Slide 1: CAT – 3 PRESENTATION TOPIC – REGISTERS AND ITS TYPES
SUBMITTED BY-
Aditya Narendra – 21SCSE1050009
ADITYA bhardwaj - 21SCSE1050014
Aditya sachan- 21SCSE1410053
Aditya pundir -21scse1410005

## Slide 2: What are registers ?
A register is a group of flip-flops capable of storing one bit of information.
Register consists of a group of flip-flops & gates that effect their transition. The flip-flops holds the binary information & the gate control when & how new information is transferred into the register.
The simplest register is that which only contains flip-flops , with no external gates.

## Slide 3: Uses of registors
While we are working on the System then these Registers are used by the CPU for Performing the Operations.
Registers Perform:-
1) Fetch: The Fetch Operation is used for taking the instructions those are given by the user and the Instructions those are stored into the Main Memory will be fetch by using Registers.
2) Decode: The Decode Operation is used for interpreting the Instructions means the Instructions are decoded means the CPU will find out which Operation is to be performed on the instructions.
3) Execute: The Execute Operation is performed by the CPU. And Results those are produced by the CPU are then Stored into the Memory and after that they are displayed on the user Screen.

## Slide 4: Types of registers
4 - bit register-
It shows how a register constructed with four D flip-flops . The common clock input triggers all flip-flops .
2. REGISTER WITH PARALLEL LOAD-
The transfer of new information into a register is referred to as loading the register .If all the bits of the register are loaded simultaneously with a common clock pulse, loading is done in parallel.
LOAD INPUT- It determines whether the next clock pulse will accept new information or leave the information in the register intact.

## Slide 5: 3. SHIFT REGISTERS-
In digital circuits a shift registeris a group of flip flops set up in a linear fashion which have their inputs and outputs connected together in such a way that the data are shifted down the line when the circuit is activated.
The simplest shift register is one that uses only flip-flops.
Shift register-The serial input determines what goes into the leftmost position during the shift.The serial output is taken from the output of the rightmost flip-flop.The clock is common to all flip-flops.
Bidirectional Shift Register with Parallel Load-A register capable of shifting in one direction only is called unidirectional shift register.A register that can shift in both directions is called bidirectional shift register.The most general shift register has all the capabilities like - input for clock pulse, shift-right operation, shift-left operation, parallel load operation, n parallel output lines, a control state.

## Slide 6: 4. BINARY COUNTERS-
A register that goes through a predetermined sequence of states upon the application of input pulses is called a counter .A counter that follows the binary number sequence is called binary counter. The main type of flip-flops used in counters are J-K flip-flops or T flip-flop.
Synchronous binary counter have a regular pattern can be seen from this figure.T flip-flops are used because set/reset ([1,0] [0,1]) functions are seldom used. Only the "do nothing" and toggle ([0,0] [1,1]) functions are used. Logic gates are used to decide when to toggle which outputs. This is an example of a 4-bit synchronous binary counter, implemented using J-K flip-flops and AND gates

## Slide 7: 5. ACCUMULATOR REGISTER-
This Register is used for storing the Results those are produced by the System. When the CPU will generate Some Results after the Processing then all the Results will be Stored into the AC Register.
6.MEMORY ADRESS REGISTER (MAR)-
This register holds the memory addresses of data and instructions. This register is used to access data and instructions from memory during the execution phase of an instruction. Suppose CPU wants to store some data in the memory or to read the data from the memory. It places the address of the-required memory location in the MAR.

## Slide 8: 7. MEMORY DATA REGISTER (MDR)-
MDR is the register of a computer’s control unit that contains the data to be stored in the computer storage (e.g. RAM), or the data after a fetch from the computer storage. It acts like a buffer and holds anything that is copied from the memory ready for the processor to use it. MDR hold the information before it goes to the decoder.
MDR which contains the data to be written into or readout of the addressed location. For example, to retrieve the contents of cell 123, we would load the value 123 (in binary, of course) into the MAR and perform a fetch operation. When the operation is done, a copy of the contents of cell 123 would be in the MDR. To store the value 98 into cell 4, we load a 4 into the MAR and a 98 into the MDR and perform a store. When the operation is completed the contents of cell 4 will have been set to 98, by discarding whatever was there previously.
The MDR is a two-way register. When data is fetched from memory and placed into the MDR, it is written to in one direction. When there is a write instruction, the data to be written is placed into the MDR from another CPU register, which then puts the data into memory.

## Slide 9: 8.INDEX REGISTER-
A hardware element which holds a number that can be added to (or, in some cases, subtracted from) the address portion of a computer instruction to form an effective address. Also known as base register. An index register in a computer’s CPU is a processor register used for modifying operand addresses during the run of a program.
9. MEMORY BUFFER REGISTER-
MBR stand for Memory Buffer Register. This register holds the contents of data or instruction read from, or written in memory. It means that this register is used to store data/instruction coming from the memory or going to the memory.
10. DATA REGISTER-
A register used in microcomputers to temporarily store data being transmitted to or from a peripheral device.

## Slide 10: THANK YOU